## Slide 1: CET 3510 Microcomputer Systems Tech. Lecture 3
Professor:
Dr. José M. Reyes Álamo

## Slide 2: Roman Numerals: I, V, X, L, C, M
Decimal
Non-positional
No zero
Arithmetic is hard
For fractions they used duodecimal, very complicated

## Slide 3: Positional Systems
Review of exponential values
  Powers of 2, 10, and 16
Each digit is a power of the base: 123 = 1*102 + 2*101 + 3*100 = 100+20+3
Easy to write fractions 123.456 = 1*102 + 2*101 + 3*100 + 4*10-1 + 5*10-2 + 6*10-3
Binary system, uses base 2: 110010102 = 20210
Each digit is a bit (short for binary digit)

## Slide 4: Base conversion
Dividing continuously by the base until reaching a quotient of 0
Listing the powers and subtracting

## Slide 5: Binary Formats
Decimal we use comas 7,547,198,334 instead of 7547198334
Book uses leading zeros and _ every 4 bits: 0001_1010_0101_0010
Low-order (least significant bit), high-order (most significant bit)

## Slide 6: Hexadecimal
Binaries are too verbose
Compact (as decimals) easy to convert to/from binary
Radix (base) is 16
Values 0,1,2,3,4,5,6,7,8,9,A (10),B (11),C(12),D(13),E(14),F(15)
Examples of conversions

## Slide 7: Bits
1’s or 0’s
Can represent anything
Data structures are used to define them

## Slide 8: Nibbles
Collection of 4 bits
Used for Binary-coded decimals (BCD) and Hexadecimal

## Slide 9: Bytes
8 bits, 256 different values
H.O. Nibble, L.O. Nibble
8-bit signed integer range: -128 to +127

## Slide 10: Word
2 bytes, 16-bits, 65,536 different values
Integers: 0…65,535 or -32,768 … 32,767
Unicode

## Slide 11: Double Word
4 bytes, 32 bits, 4,294,967,296
Range: -2,147,483,648 to 2,147,483,647
Used for floating-point and for pointers

## Slide 12: Quad Words
8 bytes, 64 bits

## Slide 13: Practice Binary and Hex Arithmetic:
Binary: 11011002 + 10001112 = ???
1016 – 116 = ???
916 + 116 = ???

## Slide 14: Numbers vs. Representation in HLA
For numbers, the default representation is in Hex
To display in Decimal need to use the appropriate library function (i.e. puti8, puti32, geti8, geti32, puth8, puth32, geth8, geth32) or define the variable as int8, int16 etc.

## Slide 15: Representing negatives in Binary
n bits can represent 2n different objects (28 = 256 objects …)
To represent negative we take half of the object 2n-1, therefore for n bits we have the range -2n-1, 2n-1-1 inclusive. ([-128, 127], [-32,768, 32,767] etc)

## Slide 16: Two’s complement
Higher order bit is the sign, 0 for positive, 1 for negative give examples
  In Hex, if left most is > 8 is negative, otherwise positive

## Slide 17: Two’s Complement Conversion Algorithm
  Switch 0’s for 1’s and 1’s for 0’s
  Add 1, ignore overflow
  i.e. -5 is 00000101  11111011 in two’s complement
  Using the first bit as a sign is known as one’s complement. Representation is easier but arithmetic is harder
  Math is easy with two’s complement

## Slide 18: Two’s Complement Note
int8, int32, etc assumes signed values.
To declare unsigned you use uns8, uns16, uns32.
To display stdout.putu8, putu16, putu32.

## Slide 19: Sign Extension
For signed values
  If leftmost value is <= 7, fill with 0’s
  If leftmost value is >= 8, fill with F’s
For unsigned values fill with 0’s
Commands: cbw, cwd, cdq, cwde

## Slide 20: More commands
Movsx(source, dest) command (move and sign extend)
  Source must be greater than dest
Movzx(source, dest) command (move and zero extend)

## Slide 21: Sign contraction and sign clipping
Not a good practice
Can incur overflow if the number is greater that the space
Trick, H.O. must be FF16 or 0016
Clipping: copy the value if it fits, otherwise set it to the maximum (losing precision)