## Slide 1: Switch Commands

## Slide 2: Basic configuration
Switch Default Gateway
switch# configure terminal
switch(config)# ip default-gateway 192.168.11.254
Switch IP Address
switch# configure terminal
switch(config)# interface vlan 1
switch(config-if)# ip add 192.168.11.254 255.255.255.0

## Slide 3: VLAN Configuration
Manually designate ports as trunk
switch#configure terminal
switch(config)#interface range fa0/8, fa0/23 – 25
switch(config-if)#switchport mode trunk
Manually designate ports as access
switch#configure terminal
switch(config)#int range fa0/8, fa0/23 – 25
switch(config-if)#switchport mode access

## Slide 4: Adding or Removing VLANs from a trunk
add | Specifies the VLANs to be added to the current list.
except | Specifies all VLANs to be added to the current list, except the specified VLANs.
remove | Specifies the VLANs to be removed from the current list.
vlan_list | VLAN IDs of the allowed VLANs when the interface is in trunking mode. The range is from 1 to 4094, except for the VLANs reserved for internal use. Use a hyphen (-) to separate the beginning and ending IDs of a range of VLAN IDs; for example, 70-100. Use a comma (,) to separate individual VLAN IDs and ranges of VLAN IDs; for example, 20,70-100,142.
all | Specifies all VLANs to be added to the current list.
none | Specifies that no VLANs be added to the current list.
switchport trunk allowed vlan
To configure the allowed VLANs for a virtual Ethernet interface, use the switchport trunk allowed vlan command. To remove the configuration, use the no form of this command.
switchport trunk allowed vlan {{ add | except | remove } vlan_list | all | none }
no switchport trunk allowed vlan
Syntax Description

## Slide 5: Adding or Removing VLANs from a trunk
Creating a list of allowed VLANs for a given trunk port
switch#conf t
switch(config)#int gi0/1
switch(config-if)#switchport mode trunk
switch(config-if)#switchport trunk allowed vlan 5-15
Removing a VLAN from the list given trunk port
switch#configure terminal
switch(config)#int gi0/1
switch(config-if)#switchport trunk allowed vlan remove 6

## Slide 6: Other commands
show run
show vlan
show int trunk
show ip route
show ip int brief