## Slide 1: FINAL STUDY GUIDE 2016

## Slide 2: List Airborne Hazards
Dust
Fume
mist
Vapor
Gas
smoke

## Slide 3: Dust
Define Respirable
Under 10 microns: deep into lung sacs
Define Non-Respirable
10-100 microns sell in sinuses and bronchial tubes

## Slide 4: What does TLV stand for?
Threshold limit value
airborne concentration of a substance below which all workers are believed to be protected while exposed to it day after day for 8-hour periods.
for fumes, mists, and dusts as milligrams per cubic meter (mg/m3) of surrounding air.

## Slide 5: PEL
Permissive exposure limit.
the maximum amount or concentration of a chemical that a worker may be exposed to under OSHA regulations

## Slide 6: ACGIH classifies TLV in three ways
TLV-TWA--Time weighted average concentration for a normal 8-hour workday or 40-hour workweek.
TLV-STEL--Short term exposure limit, or maximum concentration of a substance
TLV-C--Ceiling exposure limit or maximum exposure concentration that should not be exceeded under any circumstance, while meeting the daily TLV-TWA.

## Slide 7: Shop Safety end of day task?
Stop while crew still on clock
Clean up immediate work area
Sweep off tools
Sweep off tables
Sweep up floor
Clean out trash cans
Check in with boss before clocking out

## Slide 8: Solvents
What is a solvent?
Organic chemicals that dissolve solid materials
How do you choose a safe solvent?
Compare TLV:
higher better
Evaporation rates:
lower and slower better
Flash points;
higher better
Toxic effects
read msds

## Slide 9: solvents
Compare Threshold limit values; higher better
Compare Evaporation rates; lower and slower rates better
Compare Flash points; high better
Compare toxic effects
Compare within classes

## Slide 10: Water based vs oil based paint
Oil based
Contain solvents
Contain VOC: volatile organic chemical
Water based
May contain solvent to evaporate water
May contain VOC’s

## Slide 11: Latex paint
Toxic to environment
Contains solvents

## Slide 12: Hazards of metallic pigments
explosive

## Slide 13: Pigment Vs Dye
Dye: penetrates textile
Pigments: insoluble coat surface of textile

## Slide 14: Plastics
capable of being shaped or molded; malleability.
A polymer- long molecular chain
What happens when heated?
Fumes emitted

## Slide 15: Two part plastics resin
Bonds that link one polymer chain to another
Heat is generated by the chemical reaction that cures epoxy. A plastic mixing cup full of mixed epoxy will generate enough heat to melt the cup
What would you do to be safe?

## Slide 16: Tool safety
List two ways manufacturers try to limit risk to end users?
Manual
Grounding
Guards
Guides

## Slide 17: List a way of preventing injury with an unsafe tool
Disconnect and take out of service
Tag it and give to shop foreman
Lock out tag out

## Slide 18: Describe the lockout tag process in steps
Notify personnel
Evaluate
Shut down power source
Apply tags: must clearly state “DO NO OPERATE”
Test if energy is off
Remove guards and guides as needed
Repair
Replace guards and guides
Remove tags
Turn on power source
Test gear
Notify personnel of power on

## Slide 19: Pyrotechnics
What would you do if you were a manager of an event that wanted pyro on stage?
Permits
Local permission
Inspect location for safety
Discuss usage with staff
Use only licensed pyro technician.

## Slide 20: (Extra Credit) If you are working on a platform 6 feet or more from the surface osha requires one of three safety measure
Guard rail
Safety net
Personnel fall arrest