## Slide 1: The Americans with Disabilities Act
ADA
GROUP #3 Dominic Martinez -Introduction
Jia Rui Lin - Illustrations
Building Tech 3
Professor P. King

## Slide 2: Protection Under the ADA
Protects individuals defined as disabled:
  Physical or mental impairment that substantially impacts on one or more major life activities
  Record of such impairment
  Regarded as having such an impairment

## Slide 3: Titles of the ADA
Divided into four categories:
Employment (Title I)
State & Local Government(Title II)
Public Accommodation and Commercial Facilities(Title III)

## Slide 4: Title I: Employment
Applies to:
  Employers with more than 15 employees (excluding federal government and private clubs)
  Schools that have more than 50 employees
  Employment agencies, labor organizations and labor-management committees
  Qualified persons with a disability that are able to perform the essential functions of a job with or without reasonable accommodations

## Slide 5: Title II: Public Services
Protects against discrimination in public transportation
  Includes rail or bus services
  Excludes air travel
  Includes intercity or commuter rail services
  Excludes public school transportation

## Slide 6: Title III: Public Accommodations
Applies to:
  Hotels and motels
  Bars and restaurants
  Theaters and museums
  Stores and shopping centers
  Hospitals and professional offices
  Amusement parks and zoos
  Nurseries and private schools
  Day care centers and homeless shelters
  Gyms and health clubs

## Slide 7: What does the ADA require in new construction?
The ADA requires that all new construction of places of public accommodation, as well as of "commercial facilities" such as office buildings, be accessible. Elevators are generally not required in facilities under three stories or with fewer than 3,000 square feet per floor.
Source: Title III 2010 ADA Standards
The 2010 ADA Standards for Accessible Design set minimum requirements – both scoping and technical -- for newly designed and constructed or altered public accommodations and commercial facilities to be readily accessible to and usable by individuals with disabilities.

## Slide 8: Section 1 : Outside Regulations
The section consists of regulations that would usually appear outside the structure

## Slide 9
ADA Ramp Restrictions

## Slide 10
ADA Ramp Regulation

## Slide 11: Accessible Vehicle Space

## Slide 12: Access Path Width

## Slide 13: Section 2 : Inside Regulations
The section consists of regulations that would usually appear inside the structure

## Slide 14: Bathroom Stall Regulations 1

## Slide 15: Children’s Restroom Regulations

## Slide 16: Limits For Protruding Objects

## Slide 17: Mounted Protruding Objects

## Slide 18: Clear Space at Recessed Doors

## Slide 19: Clarification of Consecutive Doors

## Slide 20: Larger and Different Handrail Allowed

## Slide 21: ADA Stairs

## Slide 22: ADA Area Of Refuge Diagram

## Slide 23: ADA Area Of Refuge Regulations

## Slide 24: Pass Through Kitchens

## Slide 25: U-Shaped Kitchens

## Slide 26: Section 3 : Other Regulations
The section consists of regulations that would be expected on the building grounds

## Slide 27: Specific Designs for Tubs and Showers

## Slide 28: Appliance Requirements

## Slide 29: Overlapping Clearance in Residential Modification

## Slide 30: Source
http://www.access-board.gov/guidelines-and-standards/buildings-and-sites/about-the-ada-standards/background/adaag#4.13