## Slide 1: Properties of Substance & Steady State Energy Equation
Prof Akm Rahman
CC-BY-NC-SA Copyright by Prof. Dr. Akm Rahman

## Slide 2: Energy Equation for a control Mass and Control volume
This is a Control Mass Approach, where the quantity is fixed.
How about fluid flowing across the control surface?
Or Leaves with an energy per unit mass?
Energy Equation for a control mass , where mass is fixed, can be written as-

## Slide 3: Pure Substance
Homogeneous
Invariable chemical composition
Multiple phases may exist. For Example, water exists in both liquid and vapor
But chemical composition does not change.

## Slide 4: P,V,T surface for water
Change in one parameter can change other.
For example, Volume of water (Liquid/Vapor) can change with Temp or Pressure or both.
Pay Attention to critical point- Saturated liquid directly transforms into saturated vapor.
T-V diagram for water showing Liquid and Vapor Phase
P-Lines

## Slide 5: P-V-T in a 3D space
Important observation-
  How P, V, T changes simultaneously
Triple Point- Where Solid, Liquid and Vapor co-exist
Triple Point
P-V Diagram at Various T
T-Lines

## Slide 6: Example
Determine the phase for each of the following water states using the steam tables. a. 120 C, 500 kPa
b. 120 C, 0.5 m^3/kg .
Hint: Table B.1.1 is a
Saturated water table added
in the appendix of open lab.

## Slide 7: Example : Pressure Determination

## Slide 8: Steady State Energy Analysis
Steady state- Rate of change of incoming mass equals the rate of change in outgoing mass
How about fluid flowing across the control surface?
Or Leaves with an energy per unit mass?
Rate of in change in mass is constant- Steady state condition.
e= Total Energy per unit mass

## Slide 9: Terminology of Energy Equation
h=Enthalpy=u+Pv= Internal energy + Work done
P = Pressure
V= Velocity
Z= Elevation
v=specific volume
Unit of h, J/kg

## Slide 10: Steady State Process
It’s a Process where-
Example: Centrifugal air compressor

## Slide 11: Example of Steady State
Refrigeration system condenser
Heat Exchanger--- For Heat transfer
R-134 is a Refrigerant
Cold water contains cold water

## Slide 12: Analysis of Heat Exchanger
Total energy in=Total energy out
At a steady state condition-

## Slide 13: Example Problem
Given , Refrigerant (R-134 ) mi=0.2 kg/s
Find, mass flow rate of water..
How much water you need to maintain the cooling condition
(Cooling from 60 C to 35 C )?

## Slide 14: Solution

## Slide 15: How much heat is Removed from Refrigerant?
Q=m*h=(kg/s)*(KJ/kg)
    =kJ/s= kW
It can also be said-
Qr= Qw
Calculate mw
Mw Is a design Parameter that indicates-
  How many water tubes you need in the condenser
  Diameter of the tube

## Slide 16: Practice Problem
Use R-134A. Re-calculate the water mass flow rate,
using the following condition
  mr=0.3 kg/s, Refrigerant inlet condition, 70 C at 1 MPa
  Refrigerant outlet condition, 40 C at .4 MPa.
  Water inlet and outlet are 20 C and 30 C, (a) Find water mass flowrate, mw
  And (b) Heat removed from the refrigerant in kW.