## Slide 1: Roller coaster by, Mouhamath Ciss, Chun Szeto, and Danielle Alphee, Prof Kate Poirier New York City College of Technology, CUNY – Spring 2014
Abstract:
Riding Roller Coasters are an exciting and thrilling way
to spend your day. Although, you may have
many questions about them, for instance how is a
roller coaster built? We will answer this question
using calculus.
Introduction:
A roller coaster is a “small gravity railroad having a train with open cars that move along a high, sharply winding trestle built with steep inclines that produce sudden, speedy plunges for trill- seeking passengers.” Building a roller coaster has many components to it:
Slope
Turns/curves
Speed
Size
In this project we will study some conditions that are relied of how a roller coaster is built by discussing the form required for it function.
Research Question:
The first part of a roller coaster involves an ascent and descent. Given an ascent of a certain steepness and a descent of a certain steepness, what path can the roller coaster take in between so that it:
1)Looks smooth
2) And also feels smooth
Methodology:
a)This research models the structure of a real roller coaster. And for it to look smooth, we find a quadratic function in between the linear functions modeling the ascent and descent given that:
Slope of the ascent=0.8
Slope of the drop= -1.6
Distance between P and Q is 100 ft
b)To make the roller coaster feel smooth, it is
necessary to improve the first condition
because the quadratic function do not have a
continuous second derivative. For that, we
found equations who’s first two
derivatives agree and connect them between
the linear and quadratic functions
Result
a)Finding f(x), L11(x), and L2(x).
At x=0, f’(0)=2a(0)+b=0.8
b=0.8
At x=100 f’(100)=200a+0.8=-1.6
a=-0.012
And f(0)=+b(0)+c c=0
f(x)=-0.012x^2+0.8x
With derivatives: f’(x)=-0.024x+0.8
f”(x)=-0.024
We found also
L11(x)=0.8x
L2(x)=-1.6x+120
b)For the roller coaster feel smooth, we connect g(x) and h(x) between the linear and quadratic function with each in a specific domain that endpoint represent transitions points.
So L11(x)=0.8x for x<0
g(x)=kx^3+lx^2+mx+n 0≤x<10
q(x)=ax^2+bx+c 10≤x≤90
h(x)=px^3+qx^2+rx+s 90<x≤100
L2(x)=-1.6x+120 x>100
Derivatives:
L11’=0.8 L11”=0
g’(x)= 3k+2lx+m g”(x)=6kx+2l
q’(x)=2ax+b q”(x)=2a
h’(x)=3p+2qx+r h”(x)=6px+2q
L2’(x)=-1.6 L2”=0
We found at transition points:
L11(0)=g(0) 0.8(0)= k(0)+l(0)+m(0)+n n=0
L11’(0)=g’(0) 0.8=3k+2l(0)+m m=0.8
L11”(0)=g”(0) 0=6k(0)+2l l=0
At x=10
g (10)=q(10) 1000k+100l+10m+n=100a+10b+c
g’(10)=q’(10) 300k+20l+m= 20a+b
g”(10)=q”(10) 60k+2l=2a
At x=90
q (90)=h(90) 8100a+90b+c=729000p+8100q+90r+s
q’(90)=h’(90) 180a+b=24300p+180q+r
q”(90)=h”(90) 2a=540p+2q
At x=100
h(100)=L2(100) 1000000p+10000q+100r+s=-40
h’(100)=L2’(100) 30000p+200q+r=-1.6
h”(100)=L22”(100) 600p+2q=0
We compute these 12 equations that have 11 unknowns with computer algebra system
a=-1/75 b=14/15 c=-4/9
K=-1/2250 l=0 m=8/10 n=0
p=1/2250 q=-2/15 r=176/15 s=-2920/9
Then the formulas that make the roller coaster feel smooth are:
L11(x)=0.8x
g(x)=(-1/2250)x^3+(8/10)x
q(x)=(-1/75)x^2+(14/15)x-4/5
h(x)=(1/2250)x^3-(2/15)x^2+(176/15)x-(2920/9)
L 2 (x)=-1.6x+120
Conclusion:
We were able to find the formulas needed
to construct the correct slopes of the roller coaster and to create smooth transitions.