Project 1

Guidelines: Please type all the solutions! For the Smith Chart use Tools/ Typewriter to inset symbols or text. Email and UPLOAD your project 1 on your ePortfolio. In addition to this poject you also need to upload Project 2 and the reflections on the seminars/workshops/field trips, and email them to me.

Team 1:  Mamadou Bah, Arie Meiman, Daniel Edwards

- A 690λ- long lossless Z0=75Ω T-line is terminated in in a load ZL=15+j67 Ω. Calculate and use the Smith Chart  to find:

- ΓL;					b)VSWR; 					c)Zin

- The input impedance for a 100Ω lossless T-line of length 1.162λ is measured as 12+j42 Ω. Determine the load impedance.

- a) Design an open ended shunt-stub matching network to match a load ZL =70+j110 Ω to a 50 Ω  impedance T-line. Chose the solution that minimizes the length of the through line.

- Now suppose the load turns out to be ZL =40+j100 Ω. Determine the reflection coefficient seen looking into the matching network.

- A load impedance ZL=25+j90 Ω is to be matched to a 50 Ω line using a shorted shunt stub tuner. Find the solution that minimizes the length of the shorted stub

- A 50 Ω  line is terminated in a pair of parallel load impedances of 50+j100 Ω and 50 –j100 Ω. Determine the total load admittance and impedance seen by the line.

- Consider the figure with the following values VS=10V, RS=30Ω, R0=50Ω, up=0.666c, RL=150Ω, and l=10cm. Plot out to 2ns

- the voltage at the source end,

- b) the voltage at the middle,

- c) the voltage at the load end of the T-line.

Project 1

Guidelines: Please type all the solutions! For the Smith Chart use Tools/ Typewriter to inset symbols or text. Email and UPLOAD your project 1 on your ePortfolio. In addition to this poject you also need to upload Project 2 and the reflections on the seminars/workshops/field trips, and email them to me.

Team 2:  Yevgeniy Morozov, Rupan Hossain, Esnan Ambeau

- A source with 50 Ω source impedance drives a 50 Ω T-Line that is 1/8 of a wavelength long, terminated in a load ZL=50-j25 Ω. Calculate and use the Smith Chart  to find:

a)ΓL; 				b)VSWR; 			c)Zin seen by the source.

- A 1m long T-line has the following distributed parameters: R’=0.10 Ω/m, L’=1.0 µH/m, G’=10.0 µS/m, and C=10nF/m. If the line is terminated in a 25 Ω resistor in series with a 1.0nH inductor, calculate at 200MHz, ΓL and Zin.

- The input impedance for a 30cm length of lossless 100 Ω  impedance T-line operating at 2.0 GHz is Zin=92.3-j67.5 Ω. The propagation velocity is 0.7c. Determine the load impedance.

- A matching network, using a reactive element in series with a length d of T-Line, is to be used to match a 35 – j50 load to a 100 T-Line.  Find the through line length d and the value of the reactive element if (a) a series capacitor is used, and (b) a series inductor is used.

- You would like to match a 170  load to a 50  T-Line.  (a) Determine the characteristic impedance required for a quarter-wave transformer.  (b) What through-line length and stub length are required for a shorted shunt stub matching network?

- Consider the circuit in the figure with the following values: Vs = 10 V, Zs = 30 , Zo = 50 , up = 0.666c, ZL = 150 , l = 10 cm for a 10 V pulse of duration 0.4 ns.  Plot, out to 2 ns, (a) the voltage at the source end, (b) the voltage at the middle, and (c) the voltage at the load end of the T-Line.

Project 1

Guidelines: Please type all the solutions! For the Smith Chart use Tools/ Typewriter to inset symbols or text. Email and UPLOAD your project 1 on your ePortfolio. In addition to this poject you also need to upload Project 2 and the reflections on the seminars/workshops/field trips, and email them to me.

Team 3:  Mohammed Alawlaqi, Salam Seck, Romuald Ilboudo

- A 0.334λ long Z0=50 Ω T-line is terminated in a load ZL=100-j100 Ω. Calculate and use the Smith Chart to find:

a)ΓL; 				b)VSWR; 			c)Zin seen by the source.

- Suppose a Z0=50 Ω T-line is is terminated in a 100 Ω load. Determine the aquired impedance of a quarter-wave matching section of T-line.

- Suppose a 50 Ω coaxial cable made with a Teflon dielectric, that must operate  at 800MHz T-line is terminated in a ZL=10-j15 Ω. Use the Smith Chart to

a) Create a matching network by adding a reactive element at a suitable location along the T-line,

b) determine the length of the coaxial line  between the load and the capacitor,

c) determine the value of the series capacitor added to provide an impedance match.

- You would like to match a 170  load to a 50  T-Line.  (a) Determine the characteristic impedance required for a quarter-wave transformer.  (b) What through-line length and stub length are required for a shorted shunt stub matching network?

- Consider a 6 cm long 75 Ω transmission line terminated in a 125 Ω load and having a matched source impedance (Zs = 25 Ω).  Propagation velocity on the T-Line is 0.1c.  The source is a 0.4 ns square pulse of amplitude 4V.